## Slide 1
Product Features
Rice Cooker
HD3037
Technical Info.
Published by Philips Consumer Lifestyle Printed in China Copy Right Reserved Subject to modification
1 | Model | HD3037 |  |  |  | 
2 | Product Picture |  |  |  |  | 
3 | Control Mode | Electronic Control |  |  |  | 
4 | Rated voltage | 220V~50Hz |  |  |  | 
5 | Rated Power | 980W |  |  |  | 
6 | Capacity（L） | 5.0L |  |  |  | 
7 | Thickness of inner pot | 2.0mm |  |  |  | 
8 | Color of plastic part | Porcelain white |  |  |  | 

## Slide 2: Circuit Diagram
HD3037

## Slide 3
Exploding View
HD3037

## Slide 4
HD3037 Spare Part List:
No. | 12NC | Name(Chinese) | Name(English) | PCM
1 |  | 蒸汽阀装饰圈 | steam valve ornament | 620202900098
2 |  | 蒸汽阀盖 | steam valve cover | 620202110157
3 |  | 蒸汽阀座 | steam valve base | 620202110159
4 |  | 蒸汽阀密封圈 | steam valve seal | 610206010073
5 |  | 面盖 | top cover | 620202050151
6 |  | 上盖发热丝组件 | top cover heating assembly | 610201540030
7 |  | 保温座板 | warm keeping board | 620203020061
8 |  | 内锅密封圈 | inner pan seal | 610206010011
9 |  | 内盖 | inner cover | 620202050152
10 |  | 内锅 | inner pan | 620203030350
11 |  | IMD面板 | control pannel | 610203010093
12 |  | 显示板支架贴纸 | display board holder sticker | 610205540350
13 |  | 控制电路板组件 | control board assembly | 610201510097
14 |  | 电路板支架 | circute board holder | 620202100123
15 |  | 电源板组件 | power board assembly | 610201510041
16 |  | 开盖按钮 | opening cover button | 620202010033
17 |  | 按钮弹簧 | spring of button | 610204020071
18 |  | 铰链轴 | axis | 610204020015
19 |  | 铰链弹簧（右） | hinge spring(right) | 610204020013
20 |  | 铰链弹簧（左） | hinge spring(left) | 610204020014
21 |  | 铰链盖 | hinge cover | 620202060029
22 |  | 外壳罩 | outer shell cover | 620202120084
23 |  | 提手 | handle | 620202140049
24 |  | 发热盘 | heating assembly | 620201530021
25 |  | 外锅 | electronic type of outer pan | 620203030250
26 |  | 侧面发热组件 | side heating assembly | 610201540001
27 |  | 限温器组件 | Temperature Limit assembly | 620201520019
28 |  | 主温控器组件 | main thermostat assembly | 620201520008
29 |  | 外壳 | outer shell | 620203040141

## Slide 5
HD3037 Spare Part List
No. | 12NC | Name(Chinese) | Name(English) | PCM
30 |  | 底座 | bottom base | 620202110158
31 |  | 插座 | socket | 610201570004
32 |  | 量杯 | measuring cup | 620202070021
33 |  | 饭勺 | rice spoon | 620202070020
34 |  | 汤勺 | soup spoon | 620202080007
35 |  | 电源线 | power cord | 660200000077
36 |  | 蒸笼 | steamer | 620202090017
37 |  | 说明书 | DFU | 610205510104
38 |  | 单台装纸箱 | F-box | 610202510252
39 |  | 两台装纸箱 | outer carton | 610202520259
40 |  | 硅胶手套 | silicon gloves | 610207900029

## Slide 6: Illustration of Main Parts
Heating Elements |  |  | 
Name | Picture |  | Main Functions
1、Heating Plate |  |  | To be used for heating . Made of aluminum plate which is coiled by electric heating tubes; Power of the heating plate will influence the heating speed of rice cooker; Distortion of the heating element will influence heat conduction and cooking results.
Temperature Control Element |  |  | 
2.MAIN THERMOSTAT （NTC） |  |  | Applying the adverse-temp. attribute of thermistor where resistance decreases when the temperature rises.
Circuit Protection Element |  |  | 
1.Temperature Limited Assembly |  |  | It is an over-temperature protection device which functions to avoid dangers caused by the over high temperature if the cooker is working abnormally. It protects the cooker by automatically fusing when the temperature rises to a certain point and it is not resettable.

## Slide 7: Dissembling Procedures:
1、Take off steam valve | 2、Remove screws with a screw-driver
3、Remove screws on the base with screw driver | 4、Take off the plug on the base
5、Cut off binder with forceps and pull out all connectors | 6、Remove screws with a screw-driver

## Slide 8
7、remove 2 screws on the main thermostat with a screw driver | 8、remove screws used to fix heating plate with a screw driver
9、remove 3 screws on power board holder with a screw driver | 10. Remove 2 screws on the control board.
11、press with both hands to take off the press button holder | 12、Remove 2 screws on the power board

## Slide 9
13.Raise the hump on outer pot with a screw driver | 14.hold the outer pot and turn in anticlockwise direction to take off the outer pot
15.take off outer shell | 16.press the joining wedge of the control board to remove it。
17.Insert the spatula between the top cover and inner lid to separate them | 18.Remove the bars and 6 screws on the keep warm board, to separate keep warm board, sealing ring and inner lid

## Slide 10: Malfunction
2、No heating while on power | 
1、To test if the heating plate works properly with a multi-function meter | 2 If problems found, test if the bottom sensor works properly with a multi-function meter
To put wires on both sides of the heating plate with the multi-function meter on the resistance shift. If the multi-function meter shows infinite resistance, the heating plate must have problem, otherwise it is normal | To connect both sides of the bottom sensor with red and black wire. If the bottom sensor is normal, the meter shows 100 at ordinary temperature; otherwise, the bottom sensor must meet short circuiting or the circuit is cut off
3、If problems found, test if the top sensor works properly with a multi-function meter | 4、PCB errors
To connect both sides of the top sensor with red and black wire. If the bottom sensor is normal, the meter shows 100 at ordinary temperature; otherwise, the top sensor must meet short circuiting or the circuit is cut off | Heating plate won’t work when PCB is not charged with 200v voltage.
To test bottom sensor | To test top sensor
To connect both sides of the bottom sensor with red and black wire. 100 should be shown at ordinary temperature(25℃).If the resistance is small, rice cannot be cooked fully | connect both sides of the bottom sensor with red and black wire,100 should be shown at ordinary temperature(25℃).If resistance decreases or not fixed well, rice or porridge may be spilled while cooking

## Slide 11: Malfunction
3、Repair for spilling | 
（1) First, to check out the parameters of top sensor （2）Check whether the sensor on keep-warm board slacks off （3）Finally, check whether the display board is normal Procedures： | 
A、Remove the humps on the spatula with a knife to avoid danger of scratches. | B、loosen the screws on the top cover with a screw-driver
C、Insert the spatula into the slim gap between top cover and inner lid and slide it to separate top cover and inner lid | D、In picture below, the tin paper slightly sheds off which causes vague perception of the top sensor on pot temperature, thus leading to spilling
E、。The thin paper should be pasted tightly to the keep-warm board and air should be expelled as much as possible | F、To fasten the tin paper with glue in prevention of looseness

## Slide 12: Malfunction
3、Repair for spilling | 
G、Picture below shows the glue used to fasten the thin paper | H、If the thin paper doesn’t shed off, please check the parameters of top sensor by loosing the screws
R、The connector for top sensor is of black color which should not be messed up . | J、To test the top sensor with multi-function meter on 200K shift. Top sensor should be of 100K at ordinary temperature. Spilling happens when parameters of the top sensor go beyond the green zone.
K、If no problems found from the above procedures, there may be something with display board. If the display board sticker( a slice-shaped component )goes wrong, temperature limiter will fuse and spilling may happen. | 

## Slide 13: Troubleshooting
Fault | Reason | Solution
1. Rice Cooker doesn’t work | 1.No power supply is outputted from the socket | Check the power supply of the socket by having another appliance connected
 | 2.Power cord being open circuit | Check the power cord by replacing it with the a same one
 | 3.The plug isn’t fully connected | Insert the plug completely to ensure a fully connecting
 | 4.The corresponding function button is not pressed | Choose the function ,then press start button
 | 5.Temperature Limiter assembly fuses | Replace the Temperature Limiter assembly
 | 6.Heating element damages | Replace heating element and related assembly
 | 7.Bottom sensor being open circuit | Replace bottom sensor
 | 8.Bottom sensor being short circuit | Replace bottom sensor
 | 9.High temperature of bottom sensor | It is suggested to replace the PCB board if it is stilled shown over temp. even the inner pot is closely contacted with the heating element
 | 10.Top sensor being open circuit | Replace top sensor
 | 11.Top sensor being short circuit | Replace top sensor
2. Undercooked | 1.Rice and water in wrong proportion | Make right rice-water proportion under manual instruction
 | 2.Constant lid-opening while simmering | In no rush of opening lid while simmering rice
 | 3、Inner pot inappropriately placed | Move the inner pot around to ensure a well contact between inner pot and heating element
 | 4. Raffles between heating element and inner pot | Remove raffles between heating element and inner pot( with sandpaper or alcohol )
 | 5. Cook rice with fat | Clean out the fat
 | 6.Heating element deformed or unevenly heating | Repalce the heaing element
 | 7.Bottom of inner pot is deformed or not fully contacted with the heating element | Repair or replace the inner pot
 | 8.Top heating element malfunctions | Repalce top heating element
 | 9.Main thermostat malfunctions | Replace main thermostat
3、Overcooked Rice | 1.PCB board malfunctions | Replace PCB board
 | 2.Difference in rice quality | Define that whether the burning is caused by a change in rice quality
 | 3.Mian hermostat malfunctions | Replace main thermostat

## Slide 14: Troubleshooting
Fault | Reason | Solution
4. Spilled rice or porridge | 1.Inner pot is overloaded | Cook with right rice & water proportion referring to the instruction manual
 | 2.Difference in rice quality | Change for another type of rice
 | 3.Rice isn’t well rinsed | Rinse the rice
 | 4.Top sensor malfunctions | Repalce top sensor
 | 5.Top sensor is losened | Make the top sensor well fixed
5. Electricity Leakage | 1.Power cord is damaged | Replace the power cord
 | 2.Water comes into the outer pot | Clean out the water in the outer pot and put the cooker in a ventilative place for over 2 hours
 | 3.The cooker is operating in humid environment | Improve the operating circumstance
 | 4.Too much greasy dirt is left inside | Clean out the greasy dirt
 | 5.Plug earth terminal is not used or the socket is unearthed | Let the cooker be well earthed
 | 6.Insulativity of the alive components declines or interior wires damage | Check the components by meter at level of R*10M; repair or replace the defected ones
 | 7.Interior grounding wire loosens | Check the grounding wire to make it well-grounded
6.After powering on the rice cooker, all indicators glow | 1.Top sensor is broken | Replace top sensor assmebly
 | 2.Main thermostat is broken | Replace main thermostat
 | 3.The main circuit board flint carbonization | Repalce main board
7.The socket sparkles when powered on | 1.Water or other liquid food flows into the socket | Clean out the water or liquid food in the socket
 | 2.Plug and socket is oxidized or coming loose | Remove the oxidation with a knife or sandpaper, fasten the loosen parts with glue
 | 3.Fuse is burnt caused by some other reasons | Find out the reason and replace with another fuse of the same model
8.press button stuck | Function buttons on main board or the main board itself are broken | Replace the function button or main board
9.Water spills when cooked with rice of small portion | too much water | Cook in rice-water proportion under the instruction of user’s manual